## Slide 1: Victorian Coastal Monitoring Program
How to use
- “First Pass Coastal Assessment”

## Slide 2: Introduction and access to
CoastKit is available at CoastKit Victoria (mapshare.vic.gov.au)
CoastKit provides an online data repository of Victoria’s marine and coastal information.
The CoastKit ‘how to’ video series can be found on the Marine Knowledge CoastKit page. These videos explore general use of CoastKit
You can find all CoastKit datasets in the Victoria Spatial Data Library.

## Slide 3: First Pass Coastal Assessment using
This “First Pass Coastal Assessment” can be used to identify the follow information for the area of interest:
Administrative Boundaries
  Local Government Area Boundary
  Catchment Management Authority
  Registered Aboriginal Parties
Morphology and Coastal Structures
  Geomorphic Secondary Compartments
  Shoreline Type
  Shoreline Geology
  Depth Contours
  Coastal Protection Structures
Coastal Hazards: Inundation and Erosion
  Erosion Vulnerability
  Strom Surge (STM) and Sea Level Rise (SLR)

## Slide 4: Administrative Boundaries
Select ‘Planning and Administration
Expand the section (+)
  Select ‘Administrative Boundaries’
  Expand the section (+)
    Select ‘Local Government Area Boundary’
    Select ‘Catchment Management Authority’
  Select ‘Traditional Owners’
  Expand the section (+)
    Select ‘Registered Aboriginal Parties’
      Select the area of interest on the map
        A box will appear displaying the name of the Local Government Area, Catchment Management Authority and Registered Aboriginal Parties

## Slide 5: Administrative Boundaries – Video

## Slide 6: Morphology and Coastal Structures
Select ‘Shorelines’
Expand the section (+)
  Select ‘Coastal Compartments’
  Expand the section (+)
    Select ‘Geomorphic Secondary Compartments’
      This will show polygons representing areas over which sediment sharing occurs over several decades
  Select ‘Shoreline Type’
  Select ‘Shoreline Geology’
    Either select the area of interest on the map (a box will appear displaying the Shoreline Type and Shoreline Geology) or select the ( ) button next to the layer name to view the legend

## Slide 7: Morphology and Coastal Structures - Video

## Slide 8: Morphology and Coastal Structures
Select ‘Bathymetry and Topography’
Expand the section (+)
  Select ‘Depth Contours’
  Expand the section (+)
    Select the area appropriate for the location of interest (e.g. Port Phillip Bay)
      This will show the water depth around your area of interest

## Slide 9: Morphology and Coastal Structures
Select ‘Coastal Assets and Infrastructure’
Expand the section (+)
  Select ‘Coastal Protection Structures’
    Either select the individual structures on the map (a box will appear displaying the type of Coastal Protection Structure) or select the ( ) button next to the layer name to view the legend

## Slide 10: Morphology and Coastal Structures - Video

## Slide 11: Coastal Hazards: Inundation and Erosion
Select ‘Coastal Hazard Assessment’
Expand the section (+)
  Select ‘Statewide Scaled Datasets’
  Expand the section (+)
    Select ‘Erosion Vulnerability’
      Select ‘Victorian Consolidated CHA’
        This layer was developed around 2017, combining data from local coastal hazard assessments
        Either select the area of interest on the map (a box will appear displaying the erosion vulnerability risk) or select the ( ) button next to the layer name to view the legend
    Select ‘Strom Surge (STM) and Sea Level Rise (SLR)’
      ‘STM (100 year event)’ shows sea level rise plus storm surge
      ‘SLR’ shows sea level rise only

## Slide 12: Coastal Hazards: Inundation and Erosion - Video

## Slide 13: First Pass Coastal Assessment using
If you have any questions, please contact the VCMP team – vcmp@delwp.vic.gov.au